## Slide 1
Post Graduate Student Union Learning is Fun with Arduino 2017-18
Session-3
Working with the Arduino microcontroller
Engr S M Asim Ali
School of Computer Science ,
Beihang University

## Slide 2: Automated Mini City
2

## Slide 3: Mini City
Light sensitive street lights
Timed Traffic Lights
Automated Gates using proximity sensor
Cars that drive the City streets
3

## Slide 4: The Arduino UNO R3
USB (Data & Power)
Alternate Power (9V)
Digital I/O (2 – 13)
Serial Transfer (0 -1)
Analog Input (0 – 5)
5V / 9V / GND (x2)
Power Source
Jumper
Reset

## Slide 5
Compile
Upload to controller
Text Output (Serial Data)
Code Editor
Serial Monitor
Arduino
IDE
Window

## Slide 6: Arduino Code Basics
Commands and other information are sent to LED’s, motors and from sensors through digital and analog input & output pins

## Slide 7: Setup - Adding an LED

## Slide 8: Arduino Code Basics
Arduino programs run on two basic sections:
void setup() {
//setup motors, sensors etc
}
void loop() {
// get information from sensors
// send commands to motors
}

## Slide 9: Setup
The setup section is used for assigning input and outputs (Examples: motors, LED’s, sensors etc) to ports on the Arduino
It also specifies whether the device is OUTPUT or INPUT
To do this we use the command “pinMode”
9

## Slide 10: Setup
void setup() {
pinMode(9, OUTPUT);
}
http://www.arduino.cc/en/Reference/HomePage
port #
Input or Output

## Slide 11: Serial Communication
Image from http://www.ladyada.net/learn/arduino/lesson4.html

## Slide 13: Truth Tables for Boolean Algebra

## Slide 14: Loop
void loop() {
digitalWrite(9, HIGH);
delay(1000);
digitalWrite(9, LOW);
delay(1000);
}
Port # from setup
Turn the LED on
or off
Wait for 1 second
or 1000 milliseconds

## Slide 15: TASK 1
Using 3 LED’s (red, yellow and green) build a traffic light that
  Illuminates the green LED for 5 seconds
  Illuminates the yellow LED for 2 seconds
  Illuminates the red LED for 5 seconds
  repeats the sequence
Note that after each illumination period the LED is turned off!
15

## Slide 16: TASK 2
Modify Task 1 to have an advanced green (blinking green LED) for 3 seconds before illuminating the green LED for 5 seconds
16

## Slide 17: Variables
A variable is like “bucket”
It holds numbers or other values temporarily
17
value

## Slide 18: DECLARING A VARIABLE
int val = 5;
Type
variable name
assignment
“becomes”
value

## Slide 19: TASK 3
Replace all delay times with variables
Replace LED pin numbers with variables
19

## Slide 20: Using Variables
int delayTime = 2000;
int greenLED = 9;
void setup() {
pinMode(greenLED, OUTPUT);
}
void loop() {
digitalWrite(greenLED, HIGH);
delay(delayTime);
digitalWrite(greenLED, LOW);
delay(delayTime);
}
Declare delayTime
Variable
Use delayTime
Variable

## Slide 21: Using Variables
int delayTime = 2000;
int greenLED = 9;
void setup() {
pinMode(greenLED, OUTPUT);
}
void loop() {
digitalWrite(greenLED, HIGH);
delay(delayTime);
digitalWrite(greenLED, LOW);
delayTime = delayTime - 100;
delay(delayTime);
}
subtract 100 from
delayTime to gradually
increase LED’s blinking
speed

## Slide 22: Conditions
To make decisions in Arduino code we use an ‘if’ statement
‘If’ statements are based on a TRUE or FALSE question

## Slide 23: VALUE COMPARISONS
GREATER THAN
a > b
LESS
a < b
EQUAL
a == b
GREATER THAN OR EQUAL
a >= b
LESS THAN OR EQUAL
a <= b
NOT EQUAL
a != b

## Slide 24: IF Condition
asdfadsf
if(true)
{
“perform some action”
}

## Slide 25: IF Example
int counter = 0;
void setup() {
  Serial.begin(9600);
}
void loop() {
  if(counter < 10)
  {
      Serial.println(counter);
  }
  counter = counter + 1;
}

## Slide 26: TASK 4
Create a program that resets the delayTime to 2000 once it has reached 0
26

## Slide 27: Input & Output
Transferring data from the computer to an Arduino is done using Serial Transmission
To setup Serial communication we use the following
27
void setup() {
Serial.begin(9600);
}

## Slide 28: Writing to the Console
void setup() {
Serial.begin(9600);
Serial.println(“Hello World!”);
}
void loop() {}

## Slide 29: TASK 5
Modify your traffic light code so that each time a new LED is illuminated the console displays the status of the stoplight
Example
29
Advanced Green
Green
Yellow
Red
Advanced Green
...

## Slide 30: IF - ELSE Condition
asdfadsf
if( “answer is true”)
{
“perform some action”
}
else
{
“perform some other action”
}

## Slide 31
int counter = 0;
void setup() {
  Serial.begin(9600);
}
void loop() {
  if(counter < 10)
  {
      Serial.println(“less than 10”);
  }
  else
  {
      Serial.println(“greater than or equal to 10”);
      Serial.end();
  }
  counter = counter + 1;
}

## Slide 32: IF - ELSE IF Condition
asdfadsf
if( “answer is true”)
{
“perform some action”
}
else if( “answer is true”)
{
“perform some other action”
}

## Slide 33: IF - ELSE Example
int counter = 0;
void setup() {
  Serial.begin(9600);
}
void loop() {
  if(counter < 10)
  {
      Serial.println(“less than 10”);
  }
  else if (counter == 10)
  {
      Serial.println(“equal to 10”);
  }
  else
  {
      Serial.println(“greater than 10”);
      Serial.end();
  }
  counter = counter + 1;
}

## Slide 34: BOOLEAN OPERATORS - AND
If we want all of the conditions to be true we need to use ‘AND’ logic (AND gate)
We use the symbols &&
  Example
34
if ( val > 10 && val < 20)

## Slide 35: BOOLEAN OPERATORS - OR
If we want either of the conditions to be true we need to use ‘OR’ logic (OR gate)
We use the symbols ||
  Example
35
if ( val < 10 || val > 20)

## Slide 36: TASK 5
Create a program that illuminates the green LED if the counter is less than 100, illuminates the yellow LED if the counter is between 101 and 200 and illuminates the red LED if the counter is greater than 200
36

## Slide 37: INPUT
We can also use our Serial connection to get input from the computer to be used by the Arduino
int val = 0;void setup() { Serial.begin(9600); }void loop() { if(Serial.available() > 0) { val = Serial.read(); Serial.println(val); }
}

## Slide 38: TASK 6
Using input and output commands find the ASCII values of
#
1
2
3
4
5
ASCII
49
50
51
52
53
#
6
7
8
9
ASCII
54
55
56
57
@
a
b
c
d
e
f
g
ASCII
97
98
99
100
101
102
103
@
h
i
j
k
l
m
n
ASCII
104
105
106
107
108
109
110
@
o
p
q
r
s
t
u
ASCII
111
112
113
114
115
116
117
@
v
w
x
y
z
ASCII
118
119
120
121
122

## Slide 39: INPUT EXAMPLE
int val = 0;
int greenLED = 13;
void setup()
{
Serial.begin(9600);
pinMode(greenLED, OUTPUT);
}
void loop()
{
if(Serial.available()>0)
{
val = Serial.read();
Serial.println(val);
}
if(val == 53)
{
digitalWrite(greenLED, HIGH);
}
else
{
digitalWrite(greenLED, LOW);
}
}

## Slide 40: TASK 7
Create a program so that when the user enters 1 the green light is illuminated, 2 the yellow light is illuminated and 3 the red light is illuminated
40
Create a program so that when the user enters ‘b’ the green light blinks, ‘g’ the green light is illuminated ‘y’ the yellow light is illuminated and ‘r’ the red light is illuminated

## Slide 41: Task
Light Mode Video
Create a program that
  when the user enters ‘1’ all lights turn on
  when the user enters ‘2’ all lights flash
  when the user enters ‘3’ lights cycle repeatedly
  when the user enters ‘q’ or ‘e’ the lights turn off
  when + or - is pressed the speed of the LED increase or decrease

## Slide 42: BOOLEAN VARIABLES
boolean done = true;

## Slide 43: Run-Once Example
boolean done = false;
void setup()
{
Serial.begin(9600);
}
void loop()
{
if(!done)
{
Serial.println(“HELLO WORLD”);
done = true;
}
}

## Slide 44: TASK 8
Write a program that asks the user for a number and outputs the number that is entered. Once the number has been output the program finishes.
  EXAMPLE:
44
Please enter a number: 1 <enter>
The number you entered was: 1

## Slide 45: TASK 9
Write a program that asks the user for a number and outputs the number squared that is entered. Once the number has been output the program finishes.
Please enter a number: 4 <enter>
Your number squared is: 16

## Slide 46: Christmas Light Assignment No 1
Using at least 5 LEDs create a program that has at least 4 different modes
Must use if statements and user input to switch modes
Marks:
  Creativity [4 Marks]
  Working user input [2 Marks]
  Four Working modes [2 Marks]
  Instructions [1 Mark]
46