## Slide 1: Basic EE
Theory
  Charge
  Current
  Voltage
  Resistance
Practice
  Power supply
  Breadboards
  Resistor code
  Multimeters

## Slide 2: Theory: Charge
A property of particles that experience electromagnetic force
Two kinds of charge: positive and negative
Force due to charge obeys an inverse square law
Charge is measured in coulombs
Electrons and protons each have the same size charge
(but of opposite polarity)
Charge magnitude = 1.6 * 10-19 coulombs

## Slide 3: Theory: Current
Current is charge in motion
Most of the time we think about electrons moving
through metallic wires
The flow rate of charge is measured in couloumbs/second
or Amperes (Amps)
  charge/time = couloumbs/sec = Amperes
1 Amp = 1.6 * 1019 electrons / sec

## Slide 4: Theory: Voltage
Voltage is the driving force behind current
Voltage is the electrical potential energy a charge has due to
its position in space
    potential energy per unit of charge
    "path independent“
Voltage is measured in Joules/Coulomb or Volts (V)
Voltage is defined such that negatively charged particles are
pulled towards higher voltages
Potential energy can be converted into other forms of energy

## Slide 5: Theory: Resistance
Resistance is a property of materials
Resistors are electrical components with known resistance
  Resistor code
Resistors convert voltage to heat
Ohm's law describes the relationship between voltage and
current flow through a resistor
  V = I R
  V is the voltage across the resistor
  I is the current flowing through the resistor
  R is the resistance (depends upon the material)
Resistance is measured in Ohms, Ω

## Slide 6: Practice: Power Source

## Slide 7: Practice: Breadboard

## Slide 8: Practice: Resistor Code

## Slide 9: Practice: Multimeters
More detail on using multimeters
Voltage:
An across measurement:
Current:
A through measurement: